PORTABLE SANITARY OPEN-CHUTE DRUM TIPPER

PORT ELIZABETH, SOUTH AFRICA ( A new Portable Sanitary Open-Chute Drum Tipper from Flexicon features stainless steel product contact surfaces finished to sanitary standards and a wash-down motor, providing a low cost means of discharging non-dusty bulk materials from drums without cross contamination.

A single hydraulic cylinder rotates the drum to 60° beyond horizontal, discharging material onto the product chute and into a receiving vessel. The wide-diameter and polished surface of the chute allows contents of the drum to discharge freely regardless of particle size.

The unit accommodates drums of all popular sizes weighing up to 340 kg, and can discharge directly into process equipment or optional hoppers equipped with outlets for pneumatic conveying systems, flexible screw conveyors or tubular cable conveyors.

Mounted on castors with quick-action floor jacks for stable operation, the Tipper can be rolled to various use points throughout the plant, eliminating the need for multiple units.

Non-product contact surfaces are constructed of carbon steel with durable industrial coatings.

The company also produces Tip-Tite™ Drum Tippers for applications requiring total dust containment, as well as High-Lift Drum Tippers, Drum fillers, Box/Container Tippers, Bulk Bag Dischargers, Bulk Bag Conditioners, Bulk Bag Fillers, Flexible Screw Conveyors, Tubular Cable Conveyors, Pneumatic Conveying Systems, Bag Dump Stations, Weigh Batching and Blending Systems, and Engineered Plant-wide Bulk Handling Systems with automated controls.

For information contact Flexicon Africa (Pty) Ltd., PO Box 10450, Linton Grange, Port Elizabeth 6015, South Africa, +27 (0)41 453 1871, sales@flexicon.co.za, www.flexicon.co.za

| EE-0998_DSCN7033_20160912_1640_LO.jpg | (Low resolution images for reference only. For reproduction, please use high-resolution .jpg attached to e-mail.) Caption: Flexicon Portable Sanitary Open-Chute Drum Tipper with smooth, wide-diameter chute rotates the drum to 60° beyond horizontal, allowing bulk material to discharge freely regardless of particle size. |
| --- | --- |

#                     #                     #

EE-0998ZA Sanitary Open Chute Drum Tipper PR 20161013.doc

Keywords:

Drum Tipper

Open Chute Drum Tipper

Sanitary Open Chute Drum Tipper

Portable Open Chute Drum Tipper