PRESS RELEASE

Bosch Sabre saw blades make light work of steel and wood

20 October, 2016: The new Progressor for Wood and Metal series of Sabre saw blades from Bosch allows efficient cutting of various building materials by professional tradespeople carrying out demolition and renovation work.

“In construction, hardened and high-alloy steels such as stainless V2A, V4A or duplex steel are being installed increasingly in combination with wooden components,” Bosch Power Tool Accessories Senior Brand Manager Campbell Mhodi comments.

A simple example is Inox screws for fitting roof and façade elements. If these building elements have to be demolished or adjusted, it presents tradespeople with a great challenge because they cannot be cut through using standard bi-metal saw blades. This is where the Progressor for Wood and Metal series of Sabre saw blades comes into its own.

Robust and durable for the toughest applications, these saw blades have sharp carbide teeth welded onto them. In addition, the tooth strip is ‘progressive’, from which the name is derived, Mhodi explains.

The tooth spacing increases from the shank towards the blade tip. Therefore the same blade can be used to cut thin materials such as screws and thick materials such as wooden profiles simultaneously. As a result, these boast a longer lifetime than bi-metal blades.

“If you only want to cut materials made of high-alloy steel, we recommend using our ‘Endurance for Stainless Steel’ saw blades,” Mhodi notes. New to the range is a 200 mm blade for cutting through profiles and pipes with larger diameters of up to 150 mm. The existing 115 mm and 150 mm long blades have been optimised to cover a wider range of applications.

The comprehensive carbide range from Bosch also includes Sabre saw blades for drywall materials such as cement-bound fibre boards (‘Endurance for Fibre Plaster’), aerated concrete (‘Endurance for Aerated Concrete’), poroton bricks (‘Endurance for Brick’) and cast iron (‘Basic for Cast Iron’).

Ends

Notes to the Editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Bosch link to view the company’s press office.

About Bosch Power Tools 
The Power Tools Division of the Bosch Group is the world market leader for power tools, power tool accessories and measuring tools. In 2014, its roughly 19 000 associates generated sales of 4.2 billion euros, about 85 percent of which outside of Germany. With brands such as Bosch, Skil and Dremel, the division stands for customer focus and great engineering progress. The core success factors are innovative strength and pace of innovation. The division generated about 35 percent of its sales in 2014 with products that have been on the market for less than two years. In 2015, Bosch Power Tools will again launch more than 100 new products onto the German market in its four business segments power tools, accessories, measuring tools and garden tools.

The Bosch Group is a leading global supplier of technology and services. According to preliminary figures, its roughly 290,000 associates generated sales of €48.9 billion in 2014. Its operations are divided into four business sectors: Mobility Solutions, Industrial Technology, Consumer Goods, and Energy and Building Technology. The Bosch Group comprises Robert Bosch GmbH and its more than 360 subsidiaries and regional companies in some 50 countries. If its sales and service partners are included, then Bosch is represented in roughly 150 countries. This worldwide development, manufacturing, and sales network is the foundation for further growth. In 2014, Bosch applied for some 4 600 patents worldwide. The Bosch Group’s strategic goal is to deliver innovations for connected life. Bosch improves quality of life worldwide with products and services that are innovative and spark enthusiasm. In short, Bosch creates technology that is ‘Invented for life’.

Bosch Power Tools Contact Details 
Campbell Mhodi
Bosch Power Tool Accessories Senior Brand Manager
Tel: (011) 651 9600
Email:  Campbell.Mhodi @za.bosch.com 
Web: www.bosch.co.za

Media Contact

Jonathan Ducie

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 084 709 0167

Email: jonathan@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za