For further information, please contact:

Samantha Joubert, Marketing Communications Coordinator SA

Tel: +27 11 821 3602    / Fax: +27 (0) 86 681 4342

# Samantha.joubert@skf.com

For Immediate Publication

16 August 2017

SKF unveils new machinery health monitoring solutions at CONEXPO-CON/AGG 2017

SKF’s latest condition monitoring technologies are demonstrated live on a vibrating screen operating at the show

SKF used CONEXPO-CON/AGG 2017, a major exhibition for the international construction and aggregates industries, to demonstrate its latest condition monitoring technologies. Taking center stage was the SKF Multilog IMx machine health monitoring system, with the Multilog IMx-8 – an eight-channel version of this highly popular platform and SKF’s most compact, easy-to-use machine health tool to date - making its USA debut.

At this year’s event, SKF also partnered with vibrating screen manufacturer, Deister Machine Co Inc. by having an SKF Multilog IMx-16S 16-channel condition monitoring system operating on a vibrating screen located at the Deister booth. The vibrating screen operated in the booth and the IMx will provide remotely accessible machine health data in real time throughout the show at both the Deister and SKF booths.

SKF demonstrated the power of the IMx platform by monitoring an entire vibrating screen, including the bearings supporting its rotating shafts, which were monitored by SKF Copperhead vibration and temperature sensors. These sensors are also able to monitor other screen health factors such as the cloth tensioner for looseness. A loose cloth can reduce the operating efficiency of the screen.

Copperhead vibration sensor mounted on each corner of the vibrating screen, enabling real-time monitoring of the screens operational orbit or motion. Changes in the orbit at a corner could indicate a broken support spring at that position, a change in the way the material (aggregates, ore) is fed into the screen, or a blockage of the material leading to a drop in machine efficiency.

Keith Meyers, Global Industry Manager, Mining at SKF says: "Monitoring machinery in this way can detect faults before they cause permanent damage. Certainly secondary damage can also be avoided, reducing maintenance costs and allowing better planning for maintenance, which ultimately reduces downtime. The IMx platform goes one stage further by making the machine condition data available via an Internet connection to a remote monitoring site where expert analysis of machine health can be made."

2/...CONEXPO-CON/AGG 2017

2/...CONEXPO-CON/AGG 2017

## SKF is a leading global supplier of bearings, seals, mechatronics, lubrication systems, and services which include technical support, maintenance and reliability services, engineering consulting and training. SKF is represented in more than 130 countries and has around 17,000 distributor locations worldwide. Annual sales in 2015 were SEK 75 997 million and the number of employees was 46 635. www.skf.com

## ® SKF is a registered trademark of the SKF Group.
™ BeyondZero is a trademark of the SKF Group.

By: 		Sonia Laverick

Laverick Media Communications cc

Tel: +27 (0) 11 0400 818

sonia@laverickmedia.co.za / www.laverickmedia.co.za